2H cover panel
All black areas are voids
Dotted lines represent where 90 deg. angle folds should be made, away from front; resulting in an object with a 78mm x 40mm face.
34mm
21.8mm
29.5mm
26mm
40mm
3mm, 7/64 in. dia.
4.9mm
5.9mm
75.8mm

---
8H cover panel
88mm
78mm
7mm
3mm
22mm
4mm
59mm
2.5mm
19.5mm
6mm
9.2mm
15mm
hole diameter 1/8in

---
10H cover panel
“Flaps” to be folded 90 deg. along dotted lines, away from viewer; resulting in an object with a 114mm x 40mm frontal cross section.
127mm
114mm
9mm
4.5mm
hole diameter 9/64in